Electrical Resistance and Ohm’s Law Worksheet

- What is electrical resistance?

- How does the thickness of a wire affect the resistance?

- How does the length of a wire affect the resistance?

- How does the material a wire is made of affect the resistance?

- How does the temperature affect the resistance?

- State Ohm’s Law in words.

- Write the formula for current.

- What is current measured in?

- What is voltage measured in?

- What is resistance measured in?

- Solve the following problems for current.

  - 120V and 10Ω

  - 16V and 4 Ω

  - 56V and 8 Ω

  - 72 Ω and 9V

  - 10 Ω and 2V

  - 81 Ω and 3V

  - 64V and 12 Ω

  - 50 Ω and 15V

  - 35V and 7 Ω

  - 80 Ω and 10V

- What is the formula for  voltage?

- Solve the following problems for voltage.

  - 12A and 3 Ω

  - 7A and 2 Ω

  - 5 Ω and 10A

  - 6 Ω and 3A

  - 9A and 4 Ω

  - 50 Ω and 2A

  - 4 Ω and 5 V

  - 6A and 3 Ω

  - 17A and 5 Ω

  - 18A and 4 Ω

- What is the formula for resistance?

- Solve the following problems for resistance.

  - 15V and 3 Ω

  - 16 Ω and 4 V

  - 17V and 3.5 Ω

  - 80 Ω and 12 V

  - 4 Ω and 2V

  - 90V and 10 Ω

  - 150V and 15 Ω

  - 14V and 5 Ω

  - 90V and 15 Ω