Nuclear Energy Basics Reading Guide

Taken from “Nuclear Energy” New York Times 2009. Ward,  Matthew L.

## Overview

Nuclear power plants use the forces within the nucleus of an atom to generate electricity.

The first nuclear reactor was built by Enrico Fermi below the stands of Stagg Field in Chicago in 1942. The first commercial reactor went into operation in Shippingport, Pa., in December, 1957.

In its early years, nuclear power seemed the wave of the future, a clean source of potentially limitless cheap electricity. But progress was slowed by the high, unpredictable cost of building plants, uneven growth in electric demand, the fluctuating cost of competing fuels like oil and safety concerns.

Accidents at the Three Mile Island plant in Pennsylvania in 1979 and at the Chernobyl reactor in the Soviet Union in 1986 cast a pall over the industry that was deepened by technical and economic problems. In the 1980s, utilities wasted tens of billions of dollars on reactors they couldn’t finish. In the ‘90s, companies scrapped several reactors because their operating costs were so high that it was cheaper to buy power elsewhere.

But recently, in a historic shift, more than a dozen companies around the United States have suddenly become eager to build new nuclear reactors. Growing electric demand, higher prices for coal and gas, a generous Congress and a public support for radical cuts in carbon dioxide emissions have all combined to change the prospects for reactors, and many companies were ready to try again.

The old problems remain, however, like public fear of catastrophe, lack of a permanent waste solution and high construction costs. And some new problems have emerged: the credit crisis and the decline worldwide of factories that can make components. The competition in the electric market has also changed.

Nonetheless, industry executives and taxpayers are spending hundreds of millions of dollars to plan a new chapter for nuclear power in the United States and set the stage for worldwide revival.

## How It Works

Nuclear power is essentially a very complicated way to boil water.

Nuclear fuel consists of an element – generally uranium – in which an atom has an usually large nucleus. The nucleus is made up of particles called protons and neutrons. The power produces by a nuclear plant unleashed when the nucleus of one of these atoms is hit by a neutron traveling at the right speed.

The most common reaction is that the nucleus splits – an event known as nuclear fission -- and sets loose more neutrons. Those neutrons hit other nuclei and split them, too. At equilibrium – each nuclear fission producing one additional nuclear fission – the reactor undergoes a chain reaction that can last for months or even years.

When the split atom flings off neutrons, it also sends out fragments. Their energy is transferred to water that surrounds the nuclear core as heat. The fragments also give off sub-atomic particles or gamma rays that generate heat.

Depending on the plant’s design, the water is either boiled in the reactor vessel, or transfers its heat to a separate circuit of water that boils. The steam spins a turbine that turns a generator and makes electricity.

Sometimes instead of splitting, the nucleus absorbs the neutron fired at it, a reaction that turns the uranium into a different element, plutonium 239 (Pu-239). This reaction happens some of the time in all reactors. But in what are known as breeder reactors, neutrons fired at a higher force are absorbed far more often. In this process, spent uranium fuel can be recycled into Pu-239, which can be used as new fuel. But problems with safety and waste disposal have limited their use – a fuel recycling plant that operated near Buffalo for six years created waste that cost taxpayers $1 billion to clean up.

## Recent Developments: Safety and Output

In 2009, reactors are producing more electricity than ever before, about 20 percent of the kilowatt-hours used in this country, by getting more power out of old plants.

Many reactors were designed to produce more power than had been applied for. In the 1990’s, a number of companies asked the Nuclear Regulatory Commission for “uprates,’’ which allowed them to make changes, often small, that increased their output.

Nuclear plants are also running longer, in part because deregulation of the industry has given companies an incentive to get as much as they can out of each plant. A capacity factor – the percentage of power a plant could produce if it ran continuously it is actually putting out -- of 60 or 65 percent used to be common; now the norm is 90 percent. Such increases have been essential to the survival of plans like Indian Point 3 in New York, which has gone from 40 percent in the 1980s to around 90 percent now.

Safety issues have persisted, and one incident in an Ohio plant in 2002 in particular shook confidence in the safety of reactors and the quality of nuclear regulation. Regulators ordered plant operators around the country to inspect a spot in the lid of reactor vessels that was known to be prone to leaks. In the Ohio plant, the operators were shocked to find that the boric acid that is mixed into reactor water to stabilize the reaction had eaten away a chunk of carbon steel the size of a football, leaving the vessel vulnerable to a failure.

## New Designs, New Issues

On the drawing boards at government labs are all kinds of exotic designs, using graphite and helium, or plutonium and molten sodium, and making hydrogen rather than electricity. But the experts generally agree that if a reactor is ordered soon, its design changes will be evolutionary, not revolutionary.

Many of the new designs have focused on the emergency core cooling systems, where the new goal is to minimize dependency on active systems, like pumps and valves, in favor of natural forces, like gravity and natural heat circulation and dissipation.

Westinghouse is one of the companies trying to market a reactor, the AP1000. with what is called a passive approach to safety. Compared to Westinghouse designs now in service, it requires only half as many safety-related valves, 83 percent less safety-related pipe and one-third fewer pumps.

A French company called Areva is building the EPR, for European Pressurized Water Reactor, which has four emergency core cooling systems, instead of the usual two. That not only makes it less likely that all systems would fail, but would allow the plant to keep running while one of the systems is down for maintenance.

The third entry is General Electric's Economic Simplified Boiling Water Reactor, derived from its boiling water reactor design. It is tweaked for better natural circulation in case of an accident, so there will be less reliance on pumps. But three of its four potential customers have backed away.

The Nuclear Regulatory Commission is also considering a proposal that it give approval to a handful of standardized, completed designs, rather than approving each plant’s design individually after construction had begun. The hope is to cut a 10-year construction process in half.